## Slide 1
Of
Glucose, Ethanol, Growth Rate by Optical Density and CO2-Production
Introduction about Indirect Fotometric Measurement

## Slide 2
Estimation of Glucose, Ethanol by Fotometry
Concentrations of glucose and ethanol will be measured by fotometry via enzyme kits.
It`s an indirect measurement because glucose and ethanol have no absorption in the ranges of visible or UV radiation.
Concentration is measured indirect by the absorption of Coenzyme NAD+ reduced to NADH + H+ at 340 nm by oxidizing glucose or ethanol in an enzyme reaction.

## Slide 3
Ethanol + NAD+  NADH + H+ + Ethanal
ADH
ADH: Alcohol Dehydrogenase or Dehydrogenase or Oxidoreductase
:
= 1 : 1
-I
+I
-I
Estimation of Ethanol Concentration

## Slide 4
Reaction 1:
Reaction 2:
Glucose + ATP  Glucose-6-Phosphate + ADP
Glucose-6-Phosphate Gluconat-6-Phosphate
Oxidase
Kinase
Estimation of Glucose Concentration

## Slide 5
Glucose : NADH + H+ = 1 : 1
NAD+ NADH + H+
Glucose + ATP  Glucose-6-Phophate + ADP 
Gluconat-6-Phophate
Oxidase
Kinase
Estimation of Glucose Concentration

## Slide 6
Measuring at 340 nm:
Highest Absorption of NADH + H+
 No Absorption of NAD+.
Absorptionspektra of NAD+ and NADH + H+
Wavelength (nm)
Notes: Direct measurment of glucose- or ethanol concentration by fotometry isn`t possible because both chemicals have no absorption either in the visible nor in the UV range.
But if there is existing a direct dependancy in the relation of glucose or ethanol to another reaction partner which has an absorption in the visible or UV range concentration of glucose and ethanol could be measured indirect by the relationship to the reaction partner. The relationsship between metabolised glucose- or ethanol molecule and the produced NADH + H+ is in both test kits (see chemical equiations) 1 : 1.
Diagram shows that at 340 nm NAD+ isn´t absorbing UV light but NADH+H+ is highly absorbing UV light with a wavelength of 340 nm.

## Slide 7: Absorptionsspektra of NAD+ und NADH + H
Detector
Fotocell
Light Source
Monochromator
Cuvette + sample
E = ɛ ⋅ c ⋅ d
E ∼ c = f (I/I0)
Fotometry Principe

## Slide 8
Estimation of Cell Mass by Optical Density
Cell mass (number of cells) is measured by optical density (OD) at 600 nm.
Optical density (OD) is a turbidity measurement at 600 nm  yeast cells don`t absorb light at 600 nm but they are scattering and reflecting the light.

## Slide 9
Sample containing yeast cells
Light
600 nm (orange)
Estimation of Cell Mass by Optical Density (OD)
Notes: yeast cells in the sample don`t absorb light at 600 nm but they are scattering and reflecting the 600 nm, orange light.
As higher the number of yeast cells (produced biomass) as more light is reflected and scattered and as less light is direct transmitted and is reaching the detector.

## Slide 10
CO2 in parts per million (ppm) is measured by a CO2 sensor.
Estimation of CO2-Production